METHOD STATEMENT

Removal and Replacement of Industrial Tyres

Location
On Customers Site

PPE
Company Workwear, Goggles, Safety Footwear

Method

Locate machine needing work and apply hand brake and any isolator system fitted to the machine. Make sure the work area is clear of pedestrians etc.

Apply hydraulic jack, chocks and begin to elevate machine, then when at correct working height, apply blocks and chocks for safety during removal of wheels and tyres.

Inspect the wheel and tyre for type and damage (deflate if divided type/multi piece or the damage causes concern)

Remove wheel nuts/studs with air gun and remove wheel and tyre assembly, when free from fasteners, remove the wheel assembly, replace wheel with new unit and replace wheel nuts with air gun.

Apply hydraulic jack and elevate to working height, remove blocks and chocks and return machine to the ground.

Use a torque wrench and apply manufacturers recommended torque setting to torque and then re torque before returning the machine to service.(if a braked wheel the first torque can be done before lowering the vehicle)