SAFE WORKING (METHOD STATEMENT)

Repair and Replacement of Industrial Pneumatic Tyres

Two piece/Divided wheels

Location

On Customers Site

PPE

Company Workwear, Goggles, Safety Footwear, and reflective jacket, bump cap/hard hat and gloves

Method

- Locate machine needing work and apply hand brake and any isolator system fitted to the machine.								A)  Make sure the work area is clear of pedestrians etc.

- Apply hydraulic jack, lock the vehicle and begin to elevate machine, then when at correct working height, apply blocks/supports. 				A) For safety during removal of wheels and tyres.

- Safely deflate the tyre fully, remove (inner ring) wheel hub nuts/studs with air gun and remove wheel and tyre assembly when free from fasteners, remove (outer ring) rim clamping fasteners then remove both half’s of the wheel rim assembly from the tyre (removing tube/flap),

- complete puncture repairs or replace with new tyre as required, check wheel rim assembly and the associated components are fit for service then refit tyre (including tube/flap) to the wheel rim half’s, refit the (outer ring) rim clamping fasteners ensuring that all fasteners are tightened securely to the manufactures guidelines.

- Partially inflate the tyre slowly to a maximum of 15 psi then check that the tyre and all it’s components are properly seated, once correct refit the wheel and tyre assembly to the machine and refit (inner ring) wheel hub nuts/studs with air gun, continue to inflate slowly to the recommended manufactures working pressure.						A) Ensuring a safe working distance is maintained.

- Apply hydraulic jack and elevate to working height, remove supports  and chocks and return machine to the ground so the wheels just touch, apply torque wrench and apply manufacturers recommended torque setting then lower and remove the jack  							A) before returning the machine to service.

- Carry out a re torque to ensure wheel is secure.

SAFE WORKING (METHOD STATEMENT)

Removal and replacement of Industrial Tyres

(not divided type)

Location

On Customers Site

PPE

Company Workwear, Goggles, Safety Footwear, and reflective jacket, bump cap/hard hat and gloves

Method

- Locate machine needing work, apply hand brake and any isolator system fitted to the machine.

- Apply hydraulic jack, chock the vehicle and begin to elevate machine, then when at correct working height, apply block/supports for safety during removal of wheels and tyres.

- Check for type of wheel/tyre assemble, inspect tyre for faults and damage (if faulty/damaged deflate before removal) 					A) It is always safer to deflate the tyre before				     removal

- Remove wheel nuts with air gun and remove wheel and tyre assembly, when free from fasteners, replace wheel with the new unit and replace wheel nuts with air gun.

- Apply hydraulic jack and elevate to working height, remove blocks and chocks and return machine to the ground.

- Apply hydraulic jack and elevate to working height, remove supports  and chocks and return machine to the ground so the wheels just touch, apply torque wrench and apply manufacturers recommended torque setting then lower and remove the jack  				A) before returning the machine to service )

- Re torque as per recommendations before returning the machine to service.